## Slide 2: Agenda
Intro
A real-world project with real-world tasks
Solving various real-world tasks with AI
  Task
  Goals
  Solution
  Successes and Opportunities
  Lessons learned
Conclusion
Notes: Code completions… useful…

## Slide 3: Intro
Engineering Manager at Microsoft
Part of the C++ group: MSVC and C++ Development Experience
C++ is my favorite programming language
My first C++ conference was “Going Native”
Tinkering with SW and EE
  Embedded development, sound, power electronics
I am a ham: SW and HW fusion
  I got my FCC license in 2022
  APRS is my favorite digital mode

## Slide 4: Microsoft @ CppCon
Monday, Sept 15 | Tuesday, Sept 16 | Wed, Sept 17 | Thursday, Sept 18 | Friday, Sept 19
Building Secure Applications: A Practical End-to-End Approach | What’s New for Visual Studio Code: CMake Improvements and GitHub Copilot Agents | LLMs in the Trenches: Boosting System Programming with AI | MSVC C++ Dynamic Debugging: How We Enabled Full Debuggability of Optimized Code | Reflection-based JSON in C++ at Gigabytes per Second
Chandranath Bhattacharyya & Bharat Kumar 16:45 – 17:45 | Alexandra Kemper 09:00 – 10:00 | Ion Todirel 14:00 – 15:00 | Eric Brumer 14:00 – 14:30 | Daniel Lemire & Francisco Geiman Thiesen 09:00 – 10:00
 | What’s new in Visual Studio for C++ Developers in 2025 | C++ Performance Tips: Cutting Down on Unnecessary Objects | It’s Dangerous to Go Alone: A Game Developer Tutorial | Duck-Tape Chronicles: Rust/C++ Interop
 | Augustin Popa & David Li 14:00 – 15:00 | Kathleen Baker & Prithvi Okade 15:15 – 16:15 | Michael Price 16:45 – 17:45 | Victor Ciura 13:30 – 14:30
 | Back to Basics: Code Review | Connecting C++ Tools to AI Agents Using the Model Context Protocol | Take our survey, win prizes aka.ms/cppcon/llms | 
 | Chandranath Bhattacharyya & Kathleen Baker 14:00 – 15:00 | Ben McMorran 15:50 – 16:20 |  | 
 |  | Welcome to v1.0 of the meta::[[verse]]! |  | 
 |  | Inbal Levi 16:45 – 17:45 |  | 

## Slide 5: Audience questions
How many ham radio operators in the room?
How many of you are using AI tools today?
How many of you are building AI tools?
Raise you hand if yes 🤚
Keep your hand down if no 🚫

## Slide 6: Project and goals

## Slide 7: Repeater and tracker
Data modem
  Interface with repeater and tracker
Repeater
  Extend network range
Tracker
  Position tracking with accurate track representation
Off-grid: no grid, no internet, no infrastructure
  Ham radio: VHF 2m, HF 30m & 40m
Miniaturized design: 50mm x 35mm x 10mm
  Handheld and battery operated
  About 0.3W power consumption
Notes: We’re going to talk about ham radio… context

## Slide 8: Repeater and tracker
Mainboard: data modem
  MCU with DSP, AFE, LDO
  USB serial interface
Daughterboard: repeater and tracker
  MCU with BT/BLE/Wi-Fi
  GNSS receiver
  Environment sensor: temp/humidity/pressure
  Fuel gauge
  Battery charger and power path
  Buck-boost and LDO
  RTC
  Push button controller
Fig. 2 - Daughterboard PCB render
Fig.1 - Mainboard PCB render
Mainboard firmware and schematics is based on Nino TNC design (C) Nino Carrillo.
Mainboard and daughterboard design and PCB layout (C) Ion Todirel.

## Slide 9: Mainboard hardware
dsPIC33 MCU
LDO
3.3V
Flexible interconnect 1
UART1, UART2, USB_VBUS, +3.3V, TESTTX, DCD, RXT
USB-C connector
+5V, D+, D-, CC1, CC2
3.5mm TRRS Jack
RXA, TXA, PTT
USB UART
Analog FE Amp & buffer, LPF
UART1
UART2
ADC, PWM
ADPL42005
MCP2221A
MCP6004
DSPIC33EP256GP502
Flexible interconnect 2
USB_VBUS, +5V, USB CC1 & CC2

## Slide 10: Daughterboard hardware
ESP32 MCU
Li-Po battery 3.7V 6Wh
Fuel Guage U and I sampling
Battery charger
1.5A, power path
GNSS receiver
Push-button
controller
Hot-start battery
Battery
Buck-boost
2.1-5.5V to 5V
LDO
3.3V
RTC
I2C
UART3
Flexible interconnect 1
UART1, UART2, USB_VBUS, +3.3V, TESTTX, DCD, RXT
SOFT POWER-OFF
TLV70033v
ADP2503
MAX16150
BQ24075
M8Q
BQ27427
MCP7940N
CR1025
ML414H
Environment
Sensor
I2C
BME280
ESP32-WROOM-32E
Flexible interconnect 2
USB_VBUS, +5V, USB CC1 & CC2

## Slide 11: Repeater and tracker software
Encoding routines
Frame encoder
Modem mainboard
Packet encoder
Tracker
GNSS receiver
RTC
Frame decoder
n-N router
explicit router
Repeater
Low level framing interfacing with the modem
Low level free functions for
encoding data into packet components
Hardware
Environment sensor
Encoding data into packets
Use GPS data and decide when to send a packet
Packet router. Transform input packets and ready their routing into the network: insert router address, decrement hop count
Dedupe handling and filtering
Convert frames into plain text packets
Tracker
Repeater
Notes: Highlight tracket and repeater… or border!!!! Software…

## Slide 12: Tasks

## Slide 13: Tasks
GPIO planning
GPIO programming
Making C++ libraries embedded friendly
  Runtime throughput
  Memory allocations
Support UTF8 in an API designed for ASCII
GPS and Tracker simulator
Finding USB serial ports

## Slide 14: Legend

## Slide 15: Legend
Through the talk we will use these icons
AI generated icons for this presentation
Lessons Successes & Opportunities
Solution
Goals
Task
AI solution

## Slide 16: AI Tools

## Slide 17: AI tools
Web Chat Interfaces, ex: Chat GPT, Claude
Chat interfaces with development context, ex: Copilot
Integrated AI features: on the fly docs, explain error, completions
Chat in agent mode
Async Agents

## Slide 18: GPIO planning

## Slide 19: ESP32-WROOM-32E
47 pins
12 pins are GND
7 pins are unconnected
6 pin are strapping pins
  These are special purpose and control the boot
  They might be autoconfigured to be pulled up
  They should not be pulled up or down as could interrupt the boot
  EN pin needs an external pull-up resistor during normal operation
  Usually, should be avoided
4 pins are GPIO in but not out

## Slide 20: GPIO planning goals
4 x GPIO in
  Push-button interrupt, Modem: DCD, CRC and packet detection
7 x GPIO out
  3 x LEDs, 3 x power on/off control, Modem test TX
3 x UARTs
  Modem, USB serial interface, GNSS receiver & flashing
1 x I2C
  Fuel gauge, RTC, Environment sensor

## Slide 21: GPIO planning
Final AI iteration; friendly name/description generated by humans
Some of the GPIOs remapped due to PCB layout constrains
Pin | GPIO | Function | Name | Description | Subsystem
3 | n/a | swd/reset | SWD | Flashing | Flashing
4 | GPIO36 | gpio/in | PWR INT | Power push button interrupt. Can be used to turn the power off from a button press | Power
5 | GPIO39 | gpio/in | Charge State | Used to detect when the battery is charging | Power
6 | GPIO34 | gpio/in | Modem DCD | Used to detect a binary stream in the demodulator by Modem. Asserted high by the Modem. | Modem
7 | GPIO35 | gpio/in | Modem PKT | Used to detect when a packet arrives from the Modem. Asserted high by the Modem. | Modem
8 | GPIO32 | gpio/out | Modem Test TX | Enables Modem test TX for TX deviation adjustment. | Modem
9 | GPIO33 | gpio/out | GPS Enable | Used to turn the GPS module on. Off = logic low = default, on = logic high. | Power
10 | GPIO25 | uart1/tx | USB Serial | Serial communication from the USB port located on the Modem mainboard. | IO
11 | GPIO26 | uart1/rx | USB Serial | Serial communication from the USB port located on the Modem mainboard. | IO
12 | GPIO27 | gpio/out | PWR KILL | Interfaces with the push button controller to self power off. | Power
13 | GPIO14 | gpio/out | LED TX | Used to indicate TX | IO
16 | GPIO13 | gpio/out | LED RX | Used to indicate RX | IO
25 | GPIO0 | swd/boot | SWD | Flashing | Flashing
27 | GPIO16 | uart2/rx | Modem Serial | Serial communication from the Modem. | Modem
28 | GPIO17 | uart2/tx | Modem Serial | Serial communication from the Modem. | Modem
30 | GPIO18 | gpio/out | LED WL | Used to indicate BT/BLE/WI-FI wireless activity | IO
31 | GPIO19 | gpio/out | Modem Enable | Used to turn the Modem on. Off = logic low = default, on = logic high. | Power
33 | GPIO22 | i2c/sda | I2C | General purpose I2C | IO
34 | GPIO3 | uart0/rx, swd/rx | GPS Serial, SWD | Flashing. Also used for serial communication with the GPS receiver. | Flashing, GPS
35 | GPIO1 | uart0/tx, swd/tx | GPS Serial, SWD | Flashing. Also used for serial communication with the GPS receiver. | Flashing, GPS
36 | GPIO21 | i2c/scl | I2C | General purpose I2C | IO
37 | GPIO23 | n/a | n/a | Unused | n/a
Notes: What I did I have to do???

## Slide 22: GPIO planning
Successes
  After few iterations successfully generated a functional plan
  Correctly identified EN pin pull-up and capacitor to GND requirements
  Correctly identified GPIO in only pins
  Identified 3 of the 4 bootstrap pins
Opportunities
  Some models only identified SENSOR_VP (GPIO36) as GPIO input only
  Avoids using UART0 for functions other than programming
    Falsely proposes a plan that requires 4 x UARTs which the ESP32 does not have
  Suggested pull-up for GPIO0
  Inconsistently and incorrectly identified GPIO14 as a strapping pin
  Incorrectly identified 4 pins as connected to the internal flash
  Suggested GPIOs that don’t exist
Notes: Pick a few only? Limit the text these are the contexts I feeded ben: abstraction in general… cases.. System.. Broadly applicable

## Slide 23: GPIO planning lessons
Provide the context ahead as much as possible
  The more iterations the more requirements for more context later
Don’t limit to one model
What worked best
  A prompt with a picture of the pins and GPIOs, pins to avoid, input only pins
  Still required few iterations
What required most iterations
  A prompt with just the part number and IO requirements
  Iteration 1: correction on the pins connected to the flash
  Iteration 2: correction on 4 x UART ports
  Iteration 3: UART0 can be used for other purposes other than programming
  Iteration 4: reminder about the strapping pins
  Iteration 5: define explicitly which pins to avoid (lacking memory of bootstrap pins)
  Iteration 6: correction on pins that do not exist with picture of the ones that do
Notes: Conversation….learning… the agents are not just chat vbots

## Slide 24: MCU schematic
Fig. 3 - MCU layout (Autodesk Eagle) with documenting labels for the GPIO
Fig. 4 - MCU schematic with programming interface

## Slide 25: GPIO programming

## Slide 26: GPIO programming
GPIO plan
Implement initialization logic for GPIO, UART and I2C
Use ESP-IDF
Don’t use deprecated drivers
  esp_adc/adc_oneshot.h
  driver/i2c_master.h
Interfacing with Open Drain IO

## Slide 27: GPIO programming
Final AI revision
Initializing GPIO, UART and I2C
Boilerplate

## Slide 28: GPIO programming
Successes
  Fast generating the code to get something working
    Though the ESP32 platform has great samples, don’t have to leverage it
  Correctly suggested the correct configuration for interfacing with open drain IO
  Quick iterations to correct all the issues
Opportunities
  Without any context it sometimes generated Arduino code
  Used gpio_config which is a high level GPIO function
    This is fine but I typically prefer the lower-level functions
  It left the pins floating and did not set an internal pull-up or pull-down
  Did not suggest configuring the output GPIO as GPIO_MODE_INPUT_OUTPUT
  Did not fully initialize uart_config_t which generated compile errors
  Used deprecated driver/i2c.h instead of the driver/i2c_master.h
  The contents displayed in the Web Code Editor did not match the Chat response

## Slide 29: GPIO programming lessons
A good example where agentic mode can help
  Six iterations on the uart_config_t initialization error
  Four iterations to use driver/i2c_master.h with warnings and errors
A use case where the initial code generated by LLMs can be taken and iterated on by hand faster than iterating with LLMs
  Sometimes are too slow for fast iterations
The Web Code Editor mode has bugs and should be avoided
  I typically instruct the LLMs to not use it, and to provide the code inline
  Changes do not match the AI Chat response
  Rendering glitches which shows the correct code typed but it is later rewritten to an incorrect version
Notes: Where is it missing potyential context… point shy away for being too critical….the tools did not show the code making libraries AI friendly… code witter to use AI topols with

## Slide 30: Making C++ libraries embedded friendly

## Slide 31: Embedded platforms
Prototype friendly embedded platforms
World class development experience
Teensy 4.1
Raspberry Pi Pico
ESP32

## Slide 32: Making C++ libraries embedded friendly
The core libraries support the repeater and tracker
  libaprsroute: Core repeater
  libaprstrack: Tracker and packet encoding
The libraries were developed on desktop platforms
Header only libraries
Dependency only on a small subset of C++

## Slide 33: Embedded friendly goals
Must run on ESP32 and Raspberry Pi Pico
  Raspberry Pi Pico: for development purposes only
  Nice to have: Arduino, Teensy
Control over heap allocations
  OK to allocate at the start but not later
Reasonable throughput, but no hard real-time requirements
  Over a ham radio link typically no more than 10-12 packets per minute

## Slide 34: Optimization opportunities
Improving enum parsing
Reducing or eliminating copies when comparing addresses
Leveraging the small string optimization
Limiting allocations only to “data out” scenarios
High performance container agnostic APIs
Swappable container types, ex: use stack etl::vector
Swappable string type, ex: use stack etl::string
Polymorphic allocators (PMR) as an input parameter

## Slide 35: String to enum parsing
First human written version
Allocates on the heap
Memory inefficient
Coupling to std:string which has to be allocated on heap
First AI iteration
No heap usage
Container agnostic (std::string_view) with no coupling to std::string
The enum names are sorted

## Slide 36: String to enum parsing
First AI iteration
No heap usage
Container agnostic (std::string_view) with no coupling to std::string
The enum names are sorted
Second AI iteration
All enums start with qA
Fast and hand rolled

## Slide 37: String to enum parsing
Successes
  Immediately recognized optimization opportunities
  The human did not immediately recognize all enums starts with “qA”
  Provided good and safe solutions with minimum iterations
    Little input required
    Every iteration better than the last with minimal prompting
  Chat in agent mode can ensure the generated code is correct
Opportunities
  There is a bias against STL on embedded platforms
  const char* recommendation was not great
  The hashing suggestions by one model were too unreadable and complex
Notes: Why stl… context ahead of time sme models….

## Slide 38: Address comparisons
One address multiple representations
Address | Address Text | n | - | N | SSID
WIDE1-2 | WIDE | 1 | - | 2 | 0
WIDE1-2 | WIDE1 | 0 | - | 0 | 2
WIDE1 | WIDE | 1 | - | 0 | 0
WIDE1 | WIDE1 | 0 | - | 0 | 0
WIDE1 | WIDE | 1 | - | 0 | 0
WIDE2 | WIDE | 2 | - | 0 | 0
WIDE1-1 | WIDE | 1 | - | 1 | 0
WIDE2-2 | WIDE | 1 | - | 2 | 0
WIDE1-1 | WIDE | 1 | - | 1 | 0
WIDE1-1 | WIDE1 | 0 | - | 0 | 1
WIDE11-1 | WIDE1 | 1 | - | 1 | 0
WIDE11-1 | WIDE11 | 0 | - | 0 | 1
WIDE1 | WIDE | 1 | - | 0 | 0
WIDE1 | WIDE1 | 0 | - | 0 | 0
N0CALL-5 | N0CALL | 0 | - | 0 | 5
Address data structure
Address constrains
n must be in the range [1, 7]
N must be in the range [0, 7]
If N > 0, then n > 0 must also hold true
SSID must be in the range [1, 15]
If n > 0, then SSID must be 0
If SSID > 0, then n must be 0
Addresses examples
Address comparison

## Slide 39: Address comparisons
First human written version
Readable
Appends strings
Uses std::to_string
Notes: AI can do it, burt lessso.. But it’s up to you if it’s suitable… if it’s fast it’s your repsonsability to reject … that is a

## Slide 40: Address comparisons
First AI iteration
SSID not larger than 16
Avoid std::to_string
Avoid string concatenations
Notes: AI can do it, burt lessso.. But it’s up to you if it’s suitable… if it’s fast it’s your repsonsability to reject … that is a

## Slide 41: Address comparisons
First human written optimized version
No more address copies
Hand rolled
Address comparison

## Slide 42: Address comparisons
First AI iteration
Improved readability
Normalization

## Slide 43: Address comparisons
Successes
  Correct solutions with good readability
  Improved readability
Opportunities
  Generated code isn’t measured for performance
  Generated code isn’t always faster
  Unpredictable solutions, same prompt will result in different answers

## Slide 44: Lessons
Best programming models aren’t the best for everything
  One model suggested hashing with a cost char* interface
    3 x iterations with warnings about not using STL on embedded platforms
  Another model suggested hand rolled comparison with std::string view
    When asked to use <algorithm> it used std::lower_bound with a hand rolled hash
    When asked to simplify it used std::lower_bound with a sorted array
The models are non-deterministic
  In one go std::lower_bound / sorted array
Notes: My experience this time… , and you might get different answers for the same question

## Slide 45: Lessons
All code paths must be measured, what intuitively seems faster isn’t
Performance tasks are great for agentic tools
  Have good code coverage and have the AI tools run your tests
  Have a performance test that ensures no perf regressions
The more context and progress you’ve made on a task, the more AI can help
  A big functional piece of code that’s well commented works really well
Embedded platforms have come a long way; if you are using the standard library, you might already be there

## Slide 46: UTF8 support

## Slide 47: UTF8 support
Packets are made of encoded data and text
The message portion of the packet can be UTF8
Support UTF8 in an API designed for ASCII
NOCALL-5>T7SVVQ,WIDE1-1,WIDE2-1:`2(al"|[/>"3u}hello world^
from
latitude
longitude
longitude 3 bytes
message
icon
2 bytes
APRS Mic-E packet
altitude 3 bytes
course/speed 3 bytes
routing
path

## Slide 48: UTF8 support
Initial design focused on various string types and transcoding
  UTF8 internally
  Support common encodings: ASCII, UTF8, UTF16
  Take different string types: std::string, std::u8string, std::wstring
  Use codecvt to convert between types
Final design doesn’t have to handle transcoding
  Core encoding is encoding invariant and uses std::string/std::string_view
  The message is accepted as various string types and converted to bytes
  Encoded packet is returned as a sequence of bytes

## Slide 49: UTF8 support
Various ways to set a message
Various ways to encode a packet

## Slide 50: UTF8 support
Successes
  Code generated with codecvt was functional
  Recognized early codecvt is deprecated in C++17 and removed in C++20
    This was a bit of a shock, and I had to double check
  Recommended iconv and ICU
  Generated functional code for ICU
  With only 3 iterations AI can be led to the best solution
Opportunities
  Took a few iterations before recognizing codecvt is deprecated
  On Windows suggested MultiByteToWideChar/WideCharToMultiByte

## Slide 51: GPS and Tracker simulator

## Slide 52: GPS and Tracker simulator
During tracker development we need GPS data
It’s not feasible to drive around during development
Visualize and understand dynamic behavior
Parameter tweaking for accurate but efficient track representation
Create tests and find bugs

## Slide 53: GPS and Tracker simulator
Render a map
Generate a route from pairs of start lat/lon and end lat/lon
Generate lat/lon/speed track data for a route
Create a GPS simulator running real-time or accelerated
Feed GPS simulator data into the tracker and visualize it on a map

## Slide 54: GPS and Tracker simulator
Use OSM and Valhalla to generate static test data
GPS simulator uses interpolation and haversine to playback data
GPS simulator output is fed to the tracker
Tracker renders the data to a HTML/JavaScript client using a WebSocket server

## Slide 55: GPS and Tracker simulator
Successes
  Local OSM server running in a container
  Local Valhalla server running in a container
  Python script with two requests to Valhalla: route and trace_attributes
  Test data generation
  Interpolation function and haversine
  Boost ASIO and Civet WebSocket server
  Open Layers HTML/JavaScript client
Opportunities
  Difficult to complete the GPS simulator design; individual pieces ok
    Many iterations required while using 3 LLMs, no model could complete the task
  Initial code was not very readable

## Slide 56: GPS and Tracker simulator lessons
LLMs are scary good at Python, HTML and JavaScript
  Python scripts were complete in the first iteration
  Generated code for Open Layers was super easy to iterate on
LLMs aren’t so good at complex design problems requiring solving multiple subproblems
  Able to solve each individual sub-problem but not the whole problem
  Short memory
  20+ iterations each time with no good results
  Successful if scoped to smaller sub problems while the human does the design and integration
Generated code readability varies with the task complexity

## Slide 57: GPS and Tracker simulator

## Slide 58: Finding USB serial ports

## Slide 59: Finding USB serial ports
The mainboard has a USB serial interface
Programmatically find the mainboard
  This is leveraged in testing
  Used by a containerized system running the repeater
Linux only solution
Serial ports are not mounted to the same name
  udev is great but we don’t want to change the system configuration
Use unique hardware properties to identify each device
Address each mainboard even if 5 are mounted
  Some USB serial devices have empty USB descriptors

## Slide 60: Finding USB serial ports
Enumerate serial ports using udev
Extract various port information like name, serial number, description, udev path etc.
Identify and match information unique to each device, ex: serial number

## Slide 61: Finding USB serial ports
Successes
  Identified early that udev can be used to find serial ports
  Generated code to query udev
  udev filter queries were great
  JSON serialization
Opportunities
  Inconsistent and unreliable udev properties mapping
const char* manufacturer = udev_device_get_sysattr_value(usb_dev, "manufacturer");
const char* product = udev_device_get_sysattr_value(usb_dev, "product");
const char* serial = udev_device_get_sysattr_value(usb_dev, "serial");

## Slide 62: Conclusion

## Slide 63: Conclusion
LLMs are super useful in prototyping and early design and can increase productivity significantly
LLMs can help with the boiler plate, and we have lots in C++ too
Not every answer have to be perfect and complete to be useful
Some iterations can be long and frustrating
  Agents can help and shorten the iteration time
LLMs are pretty good and getting better
A level of understanding and competence is required to apply LLMs effectively
Better prompts will not likely compensate for LLMs limitations

## Slide 64: Q&A

## Slide 65: Q&A
quad
op-amp
crystal oscillator
MCU
high density
mezzanine connector
USB-C
connector
3.5mm TRRS audio jack
USB UART
mezzanine connector
LDO
5 x LEDs
MCU
GNSS receiver
Environment sensor
RTC
LDO
Buck-boost
Push-button controller
Battery charger
Fuel gauge
Load switch
Load switch
Hot start battery
high density
mezzanine connector
mezzanine connector
TVS diodes
LED (1/6)
on interface & programming interface
dual npn transistors
CR1025 Primary Lithium battery (other side)
crystal oscillator

## Slide 66: Appendix

## Slide 67: Finer grain control over allocations
Replace packet::from, packet::to with string_view
No dependency on the larger packet type
The results can be pre-allocated
Notes: Remove non AI slides? Criteria: - is this a problem I solved with an LLM - is there some lesson that I can impart using this example and no other…
- Can you fit an examplaination in the amount of time?

## Slide 68: Swappable string and containers
Can use any container type
Can use any string type
Can use PMR

## Slide 69: Small String Optimization
libaprsroute processes lots of strings but constrained to 9 bytes
Smaller strings are allocated on the stack
Stored in a small buffer within the container, usually 16 bytes
Not changes are needed for the string interface
With SSO
char data[16] = "string\0";
int length = 6;
Without SSO
char* data = new char[7];
memcpy(data, "string", 6);
data[6] = '\0'; int length = 6;
The examples above are illustrative only

## Slide 70: C++ Status on Embedded Platforms
The Arduino platform is not great for C++ development
  Artificially limited to C++11
  AVR based platforms have no standard library support
  ARM based platforms have inconsistent support: 🟨 Arduino Zero, ❌ Arduino Due
  Limited or no tooling extensibility
ESP32 and Raspberry Pi Pico have great C++20 support
  Pico has out-of-the-box and first class CMake integration in VSCode
  ESP-IDF VSCode integration is good but a little bit more esoteric
Teensy support limited to C++17, C++20 support can be hacked in
 | ESP32 | Raspberry Pi Pico | Teensy | Arduino AVR | Arduino ARM
Language Standard | ✅ C++20 | ✅ C++20 | C++17 | C++11 | C++11
Standard Library | ✅ newlibc | ✅ newlibc | ✅ newlibc | ❌ none | 🟨 limited
Notes: appendix

## Slide 71: Position tracking: “Route” as lat/lon/speed
Using Docker compose
  Docker Image: ghcr.io/gis-ops/docker-valhalla/valhalla:latest
Requests
curl -X POST "http://192.168.1.190:8002/route" -H "Content-Type: application/json" -d '{
"locations": [
{"lat": 47.6080, "lon": -122.3130},
{"lat": 47.6320, "lon": -122.2091}
],
"costing": "auto",
"directions_options": {"units": "miles"}
}’
curl -X POST "http://192.168.1.190:8002/trace_attributes" -H "Content-Type: application/json" -d '{
"shape": [
{"lat": 47.6319580078, "lon": -122.2173919678},
{"lat": 47.6319694519, "lon": -122.2151260376}
],
"costing": "auto",
"shape_match": "map_snap",
"directions_options": {"units": "miles"}
}'
Route rendering

## Slide 72: Enumerating audio devices
#include <alsa/asoundlib.h>
int card_id = -1; while (true)
{
snd_card_next(&card_id);
snd_ctl_t* ctl_handle = nullptr;
snd_ctl_open(&ctl_handle, fmt::format("hw:{}", card_id).c_str(), 0);
while (true)
{
int device_id = -1;
snd_ctl_pcm_next_device(ctl_handle, &device_id);
snd_pcm_info_t* pcm_info = nullptr;
snd_pcm_info_set_device(pcm_info, device_id);
snd_pcm_info_set_subdevice(pcm_info, 0);
snd_pcm_info_set_stream(pcm_info, SND_PCM_STREAM_CAPTURE);
snd_ctl_pcm_info(ctl_handle, pcm_info);
char* name = nullptr;
snd_card_get_name(card_id, &name);
char* long_name = nullptr;
snd_card_get_longname(card_id, &long_name);
fmt::format("hw:{},{}", device.card_id, device.device_id);
}
}
hw:0
hw:0,1
USB PnP Sound Device
C-Media Electronics Inc. USB PnP Sound Device
Notes: this is what is like using ALSA, it’s a C API
SND_PCM_STREAM_CAPTURE

## Slide 73: Volume Controls
#include <alsa/asoundlib.h>
snd_mixer_t* handle;
snd_mixer_selem_id_t* sid;
snd_mixer_open(&handle, 0);
snd_mixer_attach(handle, ("hw:" + std::to_string(device.card_id)).c_str()));
snd_mixer_selem_register(handle, nullptr, nullptr);
snd_mixer_load(handle);
snd_mixer_selem_id_malloc(&sid);
snd_mixer_selem_id_set_index(sid, 0);
snd_mixer_elem_t* elem = nullptr;
for (elem = snd_mixer_first_elem(handle); elem; elem = snd_mixer_elem_next(elem))
{
snd_mixer_selem_get_id(elem, sid);
audio_device_volume_control volume_control;
const char* control_name = snd_mixer_selem_get_name(elem);
for (int channel_id = 0; channel_id <= SND_MIXER_SCHN_REAR_CENTER; channel_id++)
{
const char* channel_name = snd_mixer_selem_channel_name(channel_id);
long min = 0, max = 100, value = 0;
snd_mixer_selem_get_playback_volume_range(elem, &min, &max);
snd_mixer_selem_get_playback_volume(elem, channel_id, &value);
}
}
hw:0
Front Left
Speaker
Notes: As far as I know this isn’t possible to do in Windows.

## Slide 74: Enumerating Serial Ports
#include <libudev.h>
udev* udev = udev_new();
udev_enumerate_add_match_subsystem(enumerate, "tty");
udev_enumerate_scan_devices(enumerate);
udev_list_entry* devices = udev_enumerate_get_list_entry(enumerate);
udev_list_entry* dev_list_entry;
udev_list_entry_foreach(dev_list_entry, devices)
{
const char* path = udev_list_entry_get_name(dev_list_entry);
udev_device* dev = udev_device_new_from_syspath(udev, path);
const char* devnode = udev_device_get_devnode(dev);
udev_device* usb_dev = udev_device_get_parent_with_subsystem_devtype(dev, "usb", "usb_device");
const char* manufacturer = udev_device_get_sysattr_value(usb_dev, "manufacturer");
const char* product = udev_device_get_sysattr_value(usb_dev, "product");
const char* serial = udev_device_get_sysattr_value(usb_dev, "serial"); }
/dev/ttyUSB0
f6a69ba44567ec119b112342ef680de7
Silicon Labs

## Slide 75: Mapping: Devices to udev
#include <libudev.h>
udev* udev = udev_new();
udev_enumerate* enumerate = udev_enumerate_new(udev);
udev_enumerate_add_match_subsystem(enumerate, "tty");
udev_enumerate_add_match_property(enumerate, "DEVNAME", p.name.c_str());
udev_enumerate_scan_devices(enumerate);
udev_list_entry* devices = udev_enumerate_get_list_entry(enumerate);
udev_device* device = udev_device_new_from_syspath(udev, udev_list_entry_get_name(devices));
udev_device* usb_device = udev_device_get_parent_with_subsystem_devtype(device, "usb", "usb_device");
const char* syspath = udev_device_get_syspath(device);
const char* usb_syspath = udev_device_get_syspath(usb_device);
Serial port to device description
/dev/ttyUSB0
udev_enumerate_add_match_subsystem(enumerate, "sound");
udev_enumerate_add_match_sysname(enumerate, fmt::format("card{}", d.card_id).c_str());
Sound card to device description
/sys/devices/pci0000:00/0000:00:14.0/usb1/1-4/1-4.1/1-4.1.2/1-4.1.2:1.0/ttyUSB0/tty/ttyUSB0
filter
card0

## Slide 76: Mapping: Serial Port to Sound Card
#include <libudev.h>
udev* udev = udev_new();
udev_device* dev = udev_device_new_from_syspath(udev, desc.path.c_str());
udev_device* usb_dev = udev_device_get_parent_with_subsystem_devtype(dev, "usb", "usb_device");
udev_device* parent_usb_dev = udev_device_get_parent_with_subsystem_devtype(usb_dev, "usb", "usb_device");
udev_enumerate* enumerate = udev_enumerate_new(udev);
udev_enumerate_add_match_parent(enumerate, parent_usb_dev);
udev_enumerate_add_match_subsystem(enumerate, "sound");
udev_enumerate_add_match_sysname(enumerate, "card*");
udev_list_entry* sibling_list_entry = nullptr;
udev_list_entry* devices = udev_enumerate_get_list_entry(enumerate);
udev_list_entry_foreach(sibling_list_entry, devices)
{
const char* path = udev_list_entry_get_name(sibling_list_entry);
udev_device* sibling_dev = udev_device_new_from_syspath(udev, path);
udev_device* sibling_usb_device=
udev_device_get_parent_with_subsystem_devtype(device, "usb", "usb_device");
}
Serial port device description to sound card mapping
/sys/devices/pci0000:00/0000:00:14.0/usb1/1-4/1-4.1/1-4.1.2/1-4.1.2:1.0/ttyUSB0/tty/ttyUSB0
/sys/devices/pci0000:00/0000:00:14.0/usb1/1-4/1-4.1/1-4.1.1/1-4.1.1:1.0/sound/card2

## Slide 77: Audio API Design
struct audio_device_info
{
std::string hw_id;
std::string plughw_id;
int card_id = -1;
int device_id = -1;
std::string name;
std::string stream_name;
std::string description;
audio_device_type type = audio_device_type::uknown;
};
struct audio_device_channel
{
std::string name;
int volume = 0;
int volume_linearized = 0;
audio_device_type type = audio_device_type::uknown;
audio_device_channel_id id = audio_device_channel_id::none;
};
struct audio_device_volume_control
{
std::string name;
std::vector<audio_device_channel> channels;
};
struct audio_device_volume_info
{
audio_device_info audio_device;
std::vector<audio_device_volume_control> controls;
};
API Usage Example Runtime Information
std::vector<audio_device_info> get_audio_devices();
bool try_get_audio_device_volume(const audio_device_info& device, audio_device_volume& volume);
bool try_set_audio_device_volume(const audio_device_info& device,
const audio_device_volume_control& control, const audio_device_channel& channel)

## Slide 78: Serial Ports API Design
struct serial_port
{
std::string name;
std::string description;
std::string manufacturer;
std::string device_serial_number;
};
std::vector<serial_port> get_serial_ports();
API Usage Example
Runtime Information

## Slide 79: Mapping API Design
struct device_description
{
int bus_number = -1;
int device_number = -1;
std::string path;
std::string hw_path;
std::string id_vendor;
std::string id_product;
std::string product;
std::string manufacturer;
int topology_depth = -1;
};
bool try_get_device_description(const audio_device_info& d, device_description& device);
bool try_get_device_description(const serial_port& d, device_description& device);
std::vector<audio_device_info> get_audio_devices(const device_description& desc);
bool try_get_serial_port(const device_description& desc, serial_port& p);
std::vector<device_description> get_sibling_audio_devices(const device_description& desc);
std::vector<device_description> get_sibling_serial_ports(const device_description& desc);
API Usage Example Runtime Information

## Slide 80: References
https://github.com/iontodirel/find_devices
https://github.com/iontodirel/matchbox_aprs
https://github.com/iontodirel/libaprs
https://github.com/iontodirel/libaprsroute
https://github.com/iontodirel/libaprstrack